## Slide 1: Lizard Localization
Vinit Saah, Joey Schnecker, Ryan Margraf, Hassan Ahmad

## Slide 2: Project Overview
Base Station #4
Receiver
Gateway
Central Compute
Base Station #1
Receiver
Gateway
Base Station #2
Receiver
Gateway
Base Station #3
Receiver
Gateway
End Device
Goal is to localize a single transmitter using multiple receivers by TDOA calculations
Approach is to break down the problem into several subtasks that can be stitched together.
Subtasks include:
  TB: Test bench setup and measurements
  LOC: Localization simulations
  DSP: Signal processing algorithm development
  UI: User Interface Design
The MVP for the final demonstration is to have a system that uses at least 2 receivers to collect data, estimate the possible positions of a transmitter, and shows a visualization of the estimations.
  2 receivers because we may not have enough hardware for to do more than that.

## Slide 3: Basic Block Diagrams
Tx
Rx (USRP)
Rx (USRP)
DSP
(Host 1)
DSP
(Host 2)
Storage
Storage
Host
Controller
Localization
UI
AWG/GPSDO
AWG/GPSDO
1
1
2
2
3
3
4
4
5
5
6

## Slide 4: Host controller – Host(DSP) interaction
Server /Client Model.
  Host Controller: Server
  Host (DSP): Client
  In same network (WIFI)
  TCP Sockets
Host Controller waits for Client to connect.
Upon connection, controller sends command to configure USRP and synchronize
Client upon configuration and synchronization performs DSP
Client then sends finish command to server
Server upon finish command retrieves stored files via SCP

## Slide 5: HOST- USRP Interaction
Tx
Rx (USRP)
DSP
(Host 1)
Storage
AWG/GPSDO
Host 1 configures USRP
  Central Frequency
  Subdev
  Channel
  Antenna
  Bandwidth
  Sample Rate
Configures Clock (External)
Configures Timing (External)
Synchronization :
  AWG : at the same moment
  GPSDO: 1 sec, Max 1 min
Receives sample with Metadata
Performs Cross correlation
Store cross correlated output in the file

## Slide 6: Host controller- Localization
Times of Arrival (from DSP)
Receiver Coordinates
Range Differences
Localization Algorithm
Estimated Location

## Slide 7: Progress: Hardware Acquisition
Two USRP-2920 Transceivers
AWG
Cables
Connectors
Cheap GPSDO
Still Needed:
PD-2 Transmitter
USRP B200 Transceivers
Expensive GPSDO

## Slide 8: Progress: Lab Testing
USRP interfacing
USRP interfacing using AWG
Receiving samples from USRP

## Slide 9: USRP received samples

## Slide 10: Progress: Localization Research
Reviewed papers on localization. Found three that presented a similar closed-form solution for 4 or more receivers.
xs =½ (STS)-1ST(Δ-2Rsd)
However, this still requires the distance between the transmitter and the reference receiver (Rs), which is unknown.
The papers differ on their solution to this. The one we got to work is the one presented in "Passive Source Localization Employing Intersecting Spherical Surfaces from Time-of-Arrival Differences" by Schau & Robinson
This closed form solution can be input into an iterative algorithm to get an even better estimate

## Slide 11: Progress: Localization Simulation
No noise
Noise Added

## Slide 12: Schedule
https://capstone-wes207.atlassian.net/jira/software/projects/CLL/boards/1/roadmap

## Slide 13: Future Plans
Phase Synchronize two USRPs using GPSDOs
Test the sample transmitter in the lab
Collect raw data from transmitter with USRP and save for later analysis
DSP for test signal to determine Time of Arrival
Determine fixes to localization simulation, then port to C++
Create a local network so each part of the system can interact

## Slide 14: Basic Block Diagrams(Obsolete)
Tx
Rx (USRP)
Rx (USRP)
DSP
(Host 1)
DSP
(Host 2)
Storage
Storage
Host
Controller
Loc Simulation
UI
AWG
GPSDO
GPSDO
1
1
2
2
2
2
3
3
4
4
5
5
6